## Slide 1
IMPORTANT INSTRUCTIONS
Please ensure below pointers are met while submitting the Idea PPT:
Kindly keep the maximum slides limit up to six (6). ( Including the title slide)
Try to avoid paragraphs and post your idea in points /diagrams / Infographics /pictures
Keep your explanation precise and easy to understand
Idea should be unique and novel.
You can only use provided template for making the PPT without changing the idea details pointers (mentioned in previous slides).
You need to save the file in PDF and upload the same on portal. No PPT, Word Doc or any other format will be supported.
Note - You can delete this slide (Important Pointers) when you upload the details of your idea portal.

## Slide 2
TITLE PAGE
Problem Statement ID – 03
Problem Statement Title- Autonomous Production Choke Controller for a Single Naturally Flowing Oil Well
Theme- Industrial Process Automation & Optimization
PS Category- Software
Student Name (Registered on portal)- Shyambaskar.S
Student ID-127156148

## Slide 3: FlowGuard-MPC: Adaptive Model-Predictive Production Choke Controller for Autonomous Safe Oil Well Optimization
Proposed Solution (Describe your Idea/Solution/Prototype)
Detailed explanation of the proposed solution:
FlowGuard-MPC Architecture: Autonomous Receding Horizon MPC operating at discrete 1-hour control intervals (Ts = 1 hr) with multi-step trajectory prediction (Np = 3 hrs).
Integrated Safety & Noise Filter: Combines exponential telemetry noise smoothing (alpha = 0.3) with a predictive Candidate Move Rejection Engine.
How it addresses the problem:
Hard Constraint Enforcement: Strictly limits choke ramp moves (|du| <= 5%/hr) and instantly voids any action predicted to breach pressure bounds (WHP >= 210, FLP >= 150, BHP >= 2850 psi).
Infeasible Target Resiliency (Scenario C): Automatically settles at the maximum safe achievable flow rate (183.15 bbl/hr) with zero safety violations.
Innovation and uniqueness of the solution:
Live Online System ID: Recursively estimates process gains (dQ/du, dWHP/du, dFLP/du, dBHP/du) live during execution without depending on static offline files.
Plug-and-Play API Compliance: Directly interfaces with Honeywell's official evaluation signature: Q, WHP, FLP, BHP = simulator.step(choke_position).

## Slide 4: TECHNICAL APPROACH
Technologies to be used (e.g. programming languages, frameworks, hardware)
Methodology and process for implementation (Flow Charts/Images/ working prototype)

## Slide 5: FEASIBILITY AND VIABILITY
Analysis of the feasibility of the idea
Potential challenges and risks
Strategies for overcoming these challenges

## Slide 6: ARTIFACTS
Relevant artifacts, such as :
  Copy of the Code Embedded
  Snaps of the solution proposal
  Dashboard snaps

## Slide 7: RESEARCH AND REFERENCES
Details / Links of the reference and research work